## Slide 1
Modern Platform-Supported Rootkits
Rodrigo Rubira Branco (@bsdaemon) & Gabriel Negreira Barbosa (@gabrielnb)
{ rodrigo.branco || gabriel.negreira.barbosa } @ intel.com
“As the area of our knowledge grows, so too does the perimeter of our ignorance”
Notes: Some poetic license is used in terminology to facilitate understanding (like we say architectural features even showing elements that are micro-architectural)

## Slide 2: Disclaimers
We don’t speak for our employer. All the opinions and information here are of our responsibility (actually no one ever saw this talk before)
The talk focus mostly in Intel Architecture. We’ll try to generalize as much as possible though – in that, probably many mistakes might happen, so…
Interrupt us if you have questions or important comments at any point.
    IMPORTANT: No, We are not part of the Intel Security Group (McAfee)

## Slide 3
Agenda
Motivation
Objectives
Current Rootkits Challenges
Wrong Assumptions
AES-NI
Cache Tricks
Miscellaneous
  NVDIMM Surprises
  ECC-based faults
  CAT/CMT
  MPX
Resources (github link)

## Slide 4
Figure Index
Huahuahuahua, you really expected that?
Most images were taken from Intel 64 and IA-32 Architectures Software Developer’s Manual Combined Volumes

## Slide 5
Motivation
A quick (but not dirty) history on why we decided to talk about this…
Notes: Aqui falaremos de como tanto o Gabriel quanto o Rodrigo tiveram ideias muito semelhantes de tecnicas de exploracao ao rever conceitos fundamentais da arquitetura com a experiencia atual

## Slide 6
Objectives
We have two main concerns in regards to computer security:
  Assumptions
  Composition
Notes: Exemplo de um assumption que pode ser mudado no futuro, seria o caso da NVDIMM e o impacto em atestacao
premisses

## Slide 7: Current Rootkit Challenges
OS dependency and security mechanisms
  Different versions of the same OS have different capabilities
  Windows platforms usually run additional defense mechanisms (such as AV). *nix-based platforms change frequently (difficult to cross-work on multiple systems)
The computer is an amazing platform, but also has lots of differences between different models
  Difficult to work across the board
  Some functionalities remain the same for many years though
  Most security tools don’t expect things to work in a different way than
  the usual expected platform-provided features

## Slide 8: Widely Known Rootkit Capabilities
Connect-back to bypass perimeter outgoing filters
Keylogging, session logging in general
Update mechanism (for deploying new functionalites)
Pivoting mechanism (for attacking additional machines within the perimeter)
We will NOT discuss any of them ;) Instead, we will abuse
the platform to hide and protect our code

## Slide 9: Platform Capabilities Covered
    Generally available architectural features (ECC, Caches, IVT, DMA)
    Modern architectural features (AES-NI, MPX, NVDIMM, CAT, CMT)
    Some tips on other architectures (along the way, nothing specific)

## Slide 10: IDT/IVT – What we will see next
Quick Introduction
Related Abuses:
  Assumption: Fixed location for IDTR target?
  Assumption: Always protected mode on dumps?
  Assumption: 32-bits only malware? (ahn??)

## Slide 11: IVT Introduction
Real-mode counterpart of the Interrupt Descriptor Table of Protected Mode
Let’s visualize the differences…

## Slide 12: IVT Introduction (2)
Notes: Reference:
http://download.intel.com/design/processor/manuals/253668.pdf. Vol. 3A. Page: 17-7.

## Slide 13: IDT 32 and 64 bits

## Slide 14: IVT Abuse – idt.py (Volatility) Where is the mode check?
if not addr_space is None and not symtab is None:
KPCR = 0xFFDFF000
if not addr_space.is_valid_address(KPCR):
print "KPCR is UNAVAILABLE"
return
idt_mem = read_value(addr_space, 'unsigned long', KPCR+0x38)
print 'IDT#\tISR\tunused_lo\tsegment_type\tsystem_segment_flag\tDPL\tP'
for i in range(0, 256):
offset = (i) * 8
LowOffset = read_value(addr_space, 'unsigned short', idt_mem+0 + offset)
selector = read_value(addr_space, 'unsigned short', idt_mem+2 + offset)
unused_lo = read_value(addr_space, 'unsigned char', idt_mem+4 + offset)
options = read_value(addr_space, 'unsigned char', idt_mem+5 + offset)
segment_type = options & 0x0f
system_segment_flag = (options & 0x10) >> 4
DPL = (options & 0x60) >> 5
P = (options & 0x80) >> 7
HiOffset = read_value(addr_space, 'unsigned short', idt_mem+6 + offset)
print '%s\t%4.4x:%4.4x%4.4x\t%x' % (str(i), selector, HiOffset, LowOffset, unused_lo),
print '\t%2.2x\t%x\t%x\t%x' % (segment_type, system_segment_flag, DPL, P)
If a malware changes IDTR but do not update the Windows structure,
it will still hook calls, but will be ‘invisible’ to Volatility
Notes: Hardcoded KPCR address and the IDTR not necessarily points there, and only 32 bits

## Slide 15: Bonus Abuse? check_idt.py (Volatility) Where is the mode check?
# hw handlers + system call check_idxs = list(range(0, 20)) + [128] if self.profile.metadata.get('memory_model', '32bit') == "32bit": idt_type = "desc_struct" else: idt_type = "gate_struct64" # this is written as a list b/c there are supposdly kernels with per-CPU IDTs # but I haven't found one yet... addrs = [self.addr_space.profile.get_symbol("idt_table")] for tableaddr in addrs: table = obj.Object(theType = 'Array', offset = tableaddr, vm = self.addr_space, targetType = idt_type, count = tblsz) for i in check_idxs: ent = table[i] if not ent: continue idt_addr = ent.Address if idt_addr != 0: if not idt_addr in sym_addrs: hooked = 1 sym_name = "HOOKED" else: hooked = 0 sym_name = self.profile.get_symbol_by_address("kernel", idt_addr) yield(i, idt_addr, sym_name, hooked)
If you hook a function, but export the target’s function symbol, it is all fine?
Notes: Linux version in the trunk:
https://code.google.com/p/volatility/source/browse/trunk/volatility/plugins/linux/check_idt.py
Supports 64 and 32 bits but the names are exported, and it is gone…
They at least check for 32/64 bits, but only some entries and for them, if a given symbol is exported, the hook is not malicious!

## Slide 16: And just for fun? Btw, also does not check mode…
https://code.google.com/p/volatility/source/browse/trunk/volatility/plugins/malware/idt.py
“# Currently we only support x86. The x64 does still have a GDT
# but hooking is prohibited and results in bugcheck. “
Notes: Malware in 64 bit needs to deal with Patchguard

## Slide 17: Disclaimer 2
We appreciate the work the guys did in Volatility, it is an interesting and useful tool
The idea of our point is to clarify that assumptions are everywhere and we need to understand what we use so we can have a better grasp on the limitations

## Slide 18: AES-NI – What we will see next
AES-NI Quick Introduction
AES-NI Abuse:
  Disabling the AES-NI instructions and handling the interrupts to backdoor AES implementations
Everyone read the PoC || GTFO released in this conference, right??
Should we skip this part?

## Slide 19: AES-NI Introduction
Intel® Advanced Encryption Standard New Instructions (AES-NI)
“What is it?
Intel® AES-NI is a new encryption instruction set that improves on the Advanced Encryption Standard (AES) algorithm and accelerates the encryption of data”.

## Slide 20: AES-NI Locking and Enabling
MSR 0x13C
Bit Description
0 Lock bit (always unlocked on boot time, BIOS sets it)
1 Not defined by default, 1 will disable AES-NI
2-32 Reserved

## Slide 21: The Code
Please, see at your magazine ;)
There is a chipsec check we created for you to check your system (also in the article and soon on chipsec github): http://github.com/chipsec/chipsec
We add a handle to the #UD and we set the MSR to disable AES-NI (we don’t let BIOS set the lock bit, so we can modify it at runtime)

## Slide 22: AES-NI Disable for other purposes
  Useful anti-disassembly mechanism (kernel driver + malware implementation)
  One can obviously use this idea to analyze a malware that counts on AES-NI
The BIOS part…

## Slide 23: JTAG-based debugger

## Slide 25: BIOS Analysis?
We start stopping the machine execution at the BIOS entrypoint. We defined some functions
to be used thru our code, such as:
get_eip(): Get the current RIP
get_cs(): Get the current CS
get_ecx(): Get the current value of RCX
get_opcode(): Get the current opcode (disassembly the current instruction)
find_wrmsr(): Uses the get_opcode() to compare with the '300f' (wrmsr opcode) and
return True if found (False if not)
search_wrmsr():
while find_wrmsr() == False: step() -> go to the next instruction (single-step)
find_aes():
while True:
step()
search_wrmsr()
if get_ecx() == '0000013c':
print "Found AES MSR"
break

## Slide 26: BIOS Analysis Tip
All BIOS we know sets its General Protection Fault (#GP) handler to just resume the execution
  Thus, if you set any MSR locks after giving the MSR the value you like, the BIOS will try to set it, will receive a #GP that it ignores and just continue happily

## Slide 27: Talking about disabled instructions
As we just saw, some instructions can be disabled…
Next Abuse:
  Disabling the fast system call handler in 64 bit machines to create a stealth syscall hook (is it ok to say hooker?)

## Slide 28: Changing subjects – check_syscall.py (Volatility)
memory_model = self.addr_space.profile.metadata.get('memory_model', '32bit')
if memory_model == '32bit':
mode = distorm3.Decode32Bits
func = "sysenter_do_call"
else:
mode = distorm3.Decode64Bits
func = "system_call_fastpath"

## Slide 29: We got inspired… Thanks!
IF the rootkit, in a 64-bit Linux machine:
- Unset: IA32_EFER.SCE
- Hook the #UD handler
- On the #UD exception, disassemble the instruction: if syscall
- Hook as wanted  - New way to hook system calls on 64 bit
Machines (should work on Windows too)
Now we claim credits for ALL instruction disabling related attacks (even
future ones!!)…
huahuahuAHUAhuAhuahuaU
Notes: Disable the IA32_EFER.SCE (set bit to 0), handle the UD. Check if the fault instruction is syscall opcode, if so, emulate and hook as wanted.
The joke:
Of course the credits are for whoever find new ones, we do hope that more people will pay attention to those kind of problems

## Slide 30: Cache – What we will see next
Cache Quick Introduction
Cache-related Abuse:
  Forcing async between cache and memory

## Slide 31: Quick Introduction
Write-back
Cache Hit, Cache Miss
Cache Eviction, Cache Fill
Notes: Cache Hit, Cache Miss, Eviction

## Slide 32: Cache Control

## Slide 33: Abusing Cache
Hide malicious code in disabled cache
  L3 disabling is possible in netburst (up to July 2006 accordingly to Wikipedia) microarchitecture (and all caches can be disabled in Atom cores)
  When L3 is enabled, malicious code is executed. When is disabled, malicious code is hidden
  Causes performance loss
  Life was easy 
Notes: Cache is micro-architectural, thus very dependent on the CPU model

## Slide 34: Cache Async
“FrozenCache – Mitigating Cold-Boot Attacks For Software-Based Full-Disk Encryption” presentation, 27C3 (2011)
A big challenge: How to prove the cache async? The author discuss some ideas (like performing the cold-boot attack as a test), but had not figured out a way to do from software
Some proposed using DMA…

## Slide 35: DMA x Cache
IO device issues a DMA request on the PCIe port
The PCI CPU Agent forwards the request to the DMA arbitrator
Cache
Cache
IA Core
IA Core
Graphics
DMI
PCI CPU Agent
PCIe
DMI
DDR
DDR
MC
1
4b
The DMA Arbitrator sends the request to the CPU/caches
If cache hit, data requested is sent to the DMA Arbitrator
The DMA Arbitrator forwards the request to the memory controller
The memory controller forwards request to DDR
A
B
DMA Arbitrator combines the A and B responses and completes the request
2a
2b
DMA Arbitrator
3b
3a
4a
Conclusion:
DMA accesses in Intel Platform is coherent ! No cache async there
Conclusion 2:
- We don’t want to point our fingers, but:
“We have x86 problems, but arm ain’t one”
Notes: If a forensics tool get the data thru DMA, it will get our hidden data from the cache as well. But cold boot and other approaches (like turning off the machine) would not work. Against DMA-related capture, VT-d is to your rescue [Joanna’s presentation: “Beyound the CPU: Defeating Hardware Based RAM Acquisition”]

## Slide 36: Cache Async – Proof Introducing Concepts
Page-walking mechanism
Notes: We only discuss how it works with PAE enabled

## Slide 37: Cache Async – Proof Introducing Concepts
Page Directory Pointer Table

## Slide 38: PDPTE Structure

## Slide 39: Theory – We prove it next
Page-walk hardware does not use cache when PAE is enabled
  Not part of the theory, but JUST FYI: If it did, we could actually create nice attacks with the async of cache and memory of the cr3 pointed memory
If we prove that, it is also proven that we can force a situation where cache and memory are not sync’ed

## Slide 40: Proofs Reminder: PoCs on github
Given the way that pagewalking works (PDPTE, cr3, etc)
Without interrupts and with only one thread we:
  We make sure that the PDPTEs are marked as write-back
  Invalidate the cache (wbinvd)
  We access the PDPTE entries, thus forcing it to the cache
  We change the present bit (not present) – given the cache hit, it changed in the cache
  We do random memory accesses, using virtual memory (forcing pagewalking to occur) – not enough accesses to fill the cache (otherwise, eviction would occur)
    The system did not crash, thus pagewalking does not use cache when PAE is enabled

## Slide 41: Now, if you don’t want the data anymore Reminder: PoCs on github
Just add a ‘invd’
  It will not write back memory
Proof:
  The same steps as before, adding the invd in the end, before returning (the system will not crash later, even after ‘eviction’ – there will be no eviction)

## Slide 42: Small consideration on FrozenCache
In the blog (http://frozencache.blogspot.com/) he uses the ordering:
“
3-) Flush the cache (thus truly overwriting the encryption key in RAM) wbinvd
4-) Add the desired RAM region to the CPU's MTRR (the 4K segment containing the key)
5-) Disable/freeze the CPU's cache (CR0.CD=1) movl %cr0, %eax orl 0x40000000, %eax movl %eax, %cr0
6-) Write the encryption key from the CPU registers to RAM (data remains in the cache, doesn't get written to memory) movq %xmm0, [X] movq %xmm1, [X+8] movq %xmm2, [X+16] movq %xmm3, [X+24]”
5 and 6 should be inverted (no-fill mode will not let cache to be filled)
It probably worked for him, because wbinvd takes time to complete (more on
It later) and thus, he had a cache hit, which will update the cache entry
Notes: 3 zeroes the cache. 4 sets the MTRRs to be WB. 5 sets the no-fill mode (nothing enters the cache, only write hits update it). 6 he reads memory (there will be no cache hits since he invalidated the cache, thus the writes are to memory not to the cache). The only theory is if wbinvd have not been completed until the rest is executed and the 6 actually hit and thus updated the cache contents… the ideal implementation would invert steps 5 and 6.

## Slide 43: Comments on ‘no-fill’ mode
If you are in no-fill mode, once you exit, it will write-back to memory
‘invd’ does not invalidate the cache entries while in the no-fill mode
  We mentioned it was performing a write-back, but it was happening because of the exit from no-fill mode
Interesting Coreboot file to take a look as well (src/cpu/intel/haswell/cache_as_ram.inc)

## Slide 44: Challenges
Besides ‘someone’ commenting out our assembly function called in the C code and we spending like 3 hours (total) analyzing something that was not even called (twice)…
wbinvd

## Slide 45: Miscellaneous – What we will see next Just sharing some other ideas…
ECC
NVDIMM
CAT/CMT
MPX
Notes: - Marking memory regions as ECC-failed to avoid inspection

## Slide 46: ECC - Introduction
ECC (Error Checking & Correction) memory was introduced to detect (and correct) common kinds of internal data corruption in data storage (memory, flash drives, etc)
ECC-capable memory controllers (workstation and servers) are able to detect and correct errors of a single bit per 64-bit word or only detect in two bits per 64-bit word

## Slide 47: ECC – Introduction (2)
Most controllers support four modes:
  Disabled
  Check-only
  Correct-error
  Correct-and-Scrub (correct on detection of errors, but periodically scrubs the memory for finding errors)
Source: SafeMem: Exploiting ECC-Memory for Detecting Memory Leaks and
Memory Corruption During Production Runs
Notes: How it will behave with DMA, memory acquisition??

## Slide 48: NVDIMM

## Slide 49: NVDIMM Surprises
How does it affect platform attestation??
How does it affect software disk-encryption technologies???

## Slide 50: New Intel Cache Technologies - CMT
CMT – Cache Monitoring Technology
  The OS/VMM can indicate a Resource Monitoring ID (RMID) for each application (or group of applications) it intends to monitor cache utilization (L3 only);
  See the cache occupancy per RMID;
  The intention is to provide better migration of applications to different sockets as needed, or to better mix applications in a given processor;
  Cache requests have the RMID tag;
  The HW thread tags are controlled by MSR, IA32_PQR_ASSOC
  The counters can be read thru the IA32_QoSEvtSel MSR
  Latest processors support 4 RMIDs per HW thread;

## Slide 51: Cache Coloring x Cache Partitioning
Cache Coloring is a software-based way to implement cache partitioning:
  You map logical addresses to physical addresses that will create a split in the cache lines between different processes
  Used by RTOS OSes to implement partitioning in hardware that do not support it

## Slide 52: New Intel Cache Technologies
CAT – Cache Allocation Technology
  Intended to enforce a cache QoS
  Does that through Dynamic Cache Partitioning based on a mask that is applied into the associative cache, thus permitting one to map certain addresses to a given cache location (changing the fixed locality of the cache associativity)

## Slide 53: MPX (Memory Protection eXtensions)
New ISA set of instructions
  Configured thru registers that define memory bounds
  Instructions executed before memory accesses (to check the bounds)
    On bound violation, #BR
Notes: Mention that we already claimed credits for disabling new instructions, but this one specifically when disabled (legacy), they will became a nop, so no game there

## Slide 54: MPX (cont.)
int main(int argc, char* argv) {
int buf[100];
return buf[argc];
}
Original Assembly (no-MPX):
movslq %edi, %rdi
movl -120(%rsp,%rdi,4), %eax
Assembly (gcc supporting MPX):
movl $399, %edx // load array length to edx
movslq %edi, %rdi // rdi contains value of argc
leaq -104(%rsp), %rax // load start address of buf to rax
bndmk (%rax,%rdx), %bnd0 // create bounds for buf
bndcl (%rax,%rdi,4), %bnd0 // check that memory access doesn’t violate buf’s low bound
bndcu 3(%rax,%rdi,4), %bnd0 // check that memory access doesn’t violate buf’s upper bound
movl -104(%rsp,%rdi,4), %eax // original memory access
Source:
https://software.intel.com/en-us/blogs/2013/07/22/intel-memory-protection-extensions-intel-mpx-support-in-the-gnu-toolchain

## Slide 55: MPX (Abuse)
Two components in a malware code:
  User-land
  Kernel-land
Kernel-land hooks #BR, user-land, uses bound exceptions as trampoline to the kernel
Kernel-land defines the flow of user-land application, inviable for AV to track the flow

## Slide 56: Conclusions
Assumptions are dangerous. When we compose a system, lots of assumptions are part of the final design
The architecture is well defined, but complex. Software on top of that, even more
SGX (already discussed past year) and other technologies will change the way we imagine computer forensics, it is time to evolve!

## Slide 57: Resources
All the code discussed will be available at:
https://github.com/rrbranco/Troopers2015
We will update it with other ideas that we had no time to implement/test thus we did not present
Latest PoC || GTFO has the AES-NI part, but we will put it there as well ;)

## Slide 58
The end! Really is??
Rodrigo Rubira Branco (@bsdaemon) & Gabriel Negreira Barbosa (@gabrielnb)
{ rodrigo.branco || gabriel.negreira.barbosa } @ intel.com
“As the area of our knowledge grows, so too does the perimeter of our ignorance”